## Slide 1: Geospatial analysis in R: Part 1
Michael Otterstatter BCCDC Biostats Session
Sept 6, 2019

## Slide 2: Session Overview
Background and concepts
  geospatial analysis in public health
  spatial data
  coordinate reference systems and projection systems
  Spatial data in R

## Slide 3: Background and concepts

## Slide 4: Geospatial analysis in public health
A foundation of epidemiology and public health is the identification and analysis of disease patterns in populations in terms of person, place and time, in order to:
  track diseases
  detect changes and outbreaks
  evaluate interventions and services
  prevent and control disease
The key element of place identifies where a health event of interest occurred
  Geospatial analysis is the set of methods and tools we use to describe and understand patterns in the location of health events
Background and concepts

## Slide 5: Geospatial analysis in public health
The mapping of health events has a long history in epidemiology, going back at least as far as John Snow’s mapping of cholera cases in London work during the 1850s
Background and concepts
https://upload.wikimedia.org/wikipedia/commons/2/27/Snow-cholera-map-1.jpg

## Slide 6: Geospatial analysis in public health
Modern applications in public health include,
  evaluate differences in health services and health-related rates/risk across different geographic areas
  quantify uncertainty in spatial measures/maps
  identify “clusters” of disease or other health events of interest
  assess the significance of factors potentially related to disease occurrence (e.g., exposures, services, etc.)
Background and concepts

## Slide 7: Spatial data
Spatial data are those data located in two or more dimensions – these additional dimensions provide information to better analyze and understand your data
The actual location of something is described using a georeference, typically a coordinate system
Background and concepts

## Slide 8: Coordinate reference systems (CRS)
How do we describe locations (the ‘coordinates’) of our data on the surface of the earth?
a coordinate reference system (CRS) represents locations by coordinate pairs, indicating distance from an origin point
  geographic CRS: based on latitude (degrees north/south of the equator) and longitude (degrees east/west of Prime Meridian) – every point on Earth is defined by a lat-lon coordinate pair, often written in degrees, minutes and seconds (DMS) or decimal degrees (DD)
  projected CRS: based on units (typically meters) from an origin point (a ‘datum’)
Background and concepts

## Slide 9: Projection systems
If we simply laid flat the Earth’s curved surface, spatial locations would be warped
Instead, to display spatial information defined by coordinates, we use a transformation (projection), converting location on the Earth’s surface to a location on a flat two-dimensional map
Background and concepts

## Slide 10: Projection systems
one consequence of projecting is that scale (map distance:actual distance) is not the same across a map’s surface – reported scales are usually an average
Background and concepts
https://en.wikipedia.org/wiki/Map_projection

## Slide 11: Projection systems
Many projection systems exist, with differing strengths/ weakness and degrees of warping
  conformal - preserves spatial shape over small areas, but larger areas are distorted (e.g., ‘Mercator’)
  equal area - preserves area so that relative sizes of regions are correct and comparable (e.g., ‘Albers’ equal-area’)
  equidistance - preserves distance measures
Background and concepts

## Slide 12: Projection systems
If the purpose is only a quick map, projection of spatial data is not strictly necessary – simple display of lat-lon is adequate
However, if analyses involve measures/comparisons of distance, shape or area, a projected coordinate system must be used
Choice of the projection system depends on what aspects (e.g., distance) must be most accurately preserved
Background and concepts

## Slide 13: Vectors and rasters
Vector data: representation of geographic features as points, lines, and polygons using coordinate pairs and ordered lists of vertices; attributes may be associated with each vector feature
  e.g., summarised population characteristics (e.g., health, socio-demography, etc.) by census regions or other distinct boundaries
Background and concepts

## Slide 14: Vectors and rasters
Raster data: geographic features are represented and stored as uniformly sized pixels; attributes are typically associated with each of these grid cells
  e.g., satellite imagery and other remote sensing information
Both vector and raster data can be used together (or converted from one to the other), but vector data usually require much less computational memory and time
Background and concepts

## Slide 15: Points vs areal units
Spatial information comes in a variety of forms, with space treated as
  a continuous distribution, giving rise to point data with values that can occur at any location in space (e.g., continuous measures of temperature for all points within a region); or,
  aggregate, or areal, units with summary values for each unit (e.g., average temperature in a region) which may be then assigned to a representative point such as the region’s centroid
Background and concepts

## Slide 16: Sources of spatial data in public health
health data (e.g., outcome data from routine surveillance programs, administrative health databases, observational and experimental research studies), including vital statistics, reportable diseases, disease registries, national and provincial health surveys
census data (e.g., socio-demographic information collected through formal government census), including population sizes by age, sex, region, counts of housing units, employment and income profiles, education, immigration, family sizes
environmental data (e.g., ecological indicators and natural resources routinely monitored by government and other national/provincial organizations), including land use and related characteristics, habitats, agricultural operations and practices, bodies of water and water quality, air quality, climate
remote sensing data (e.g., aerial and satellite imagining data) including, aerial photographs, satellite measures of radiation and sea-surface temperature
Background and concepts

## Slide 17: Considerations and cautions
Interpretation of spatial data has certain challenges (modifiable areal unit problem, location uncertainty, ecologic fallacy, etc.) that must be considered carefully
Different data sources may use different projection systems – these must be reconciled before data sources can be combined for analysis
specific location information, e.g., street address or corresponding coordinates, can uniquely identify individuals -- care is needed when storing and analyzing such information and it may be necessary to mask locations to protect privacy
Background and concepts

## Slide 18: Spatial data in R

## Slide 19: Background
R is a free, open-source statistical software package that can be used for all aspects of data manipulation, analysis and visualisation (https://cran.r-project.org/)
  R functions (commands) are organized into packages (also called libraries) that can be loaded as needed
  Most R users interface with the R program via RStudio and use command-line code (scripts)
Numerous R packages exist for working with spatial data (see: https://cran.r-project.org/web/views/Spatial.html)
  Here, we focus on the new sf (‘simple features’) package (see: https://CRAN.R-project.org/package=sf)
Spatial data in R

## Slide 20: The sf package
The sf package is a collection of tools for working with spatial data in R, where ‘sf’ refers to simple features, which are a standard set of geometry types (e.g., point, line, polygon, etc.) supported by the package
sf currently supports tools for vector data only (not raster data)
use of the sf package is described extensively in the free online book Geocomputation with R (https://geocompr.robinlovelace.net/)
Spatial data in R

## Slide 21: The sf package
sf data objects appear in R as standard data frames, except with addition of a geometry column containing condensed list of all coordinate information for a particular spatial feature
With a basis in standard data frames, powerful data manipulation tools of R, particularly those in the tidyverse, can be used with sf
Spatial data in R

## Slide 22: The sf package
For example, we can work with sf data objects in the same way as any (tidy) data object in R, including chaining commands together (piping) with %>%, using filter to include only certain rows, select to include only certain columns, and mutate to create new derived variables:
world_asia <- world_data %>%
filter(continent == "Asia") %>%
select(name, continent) %>%
mutate(map_col = ifelse(name == “China”, “white”, “grey”))
Spatial data in R

## Slide 23: The sf package
sf contains numerous functions (commands) for importing, manipulating, transforming and exporting spatial data – all have intuitive names and begin with the prefix st_
  st_read reads spatial data
  st_point creates spatial points
  st_crs retrieves the data’s coordinate reference system
  st_distance calculates Euclidean distance
  etc.
Spatial data in R